## Slide 1: Exposing Errors Related to Weak Memory in GPU Applications
Tyler Sorensen
Imperial College London
Supervisor: Alastair F. Donaldson
PLDI 2016

## Slide 2: Example
GPU dot product

## Slide 3: Example
__global__ void dot(int *mutex, float *a, float *b, float *c) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
float temp = 0;
while (tid < N) {
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// local computation code omitted
if (threadIdx.x== 0) {
lock(mutex);
*c += cache[0];
unlock(mutex);
}
}
__device__ void lock(int *mutex) {
while (atomicCAS(l, 0, 1) != 0 );
}
__device__ void unlock(int *mutex) {
atomicExch(l, 0);
}
GPU dot product

## Slide 4: Example
Testing the code:
  Run for 1 hour (~2 seconds per run) and check for errors
GPU dot product

## Slide 5: Example
Testing the code:
  Run for 1 hour (~2 seconds per run) and check for errors
No errors observed! Code is probably correct right?
GPU dot product

## Slide 6: Example
Testing the code:
  Run for 1 hour (~2 seconds per run) and check for errors
No errors observed! Code is probably correct right?
Wrong! Weak memory bug reported in previous work
GPU dot product

## Slide 7: Example
Previous bug found through hand analysis by experts
This is laborious and no guarantees
GPU dot product

## Slide 8: Example
Our goals:
GPU dot product

## Slide 9: Example
Our goals:
  Create a method for programmers to find bugs
GPU dot product

## Slide 10: Example
Our goals:
  Create a method for programmers to find bugs
  Automatically suggest bug fixes
GPU dot product

## Slide 11: Example
Developed a stress/fuzz testing environment
  Run for 1 hour (~2 seconds per run) and check for errors
GPU dot product

## Slide 12: Example
Developed a stress/fuzz testing environment
  Run for 1 hour (~2 seconds per run) and check for errors
  396 erroneous runs observed
GPU dot product

## Slide 13: Example
How to fix the bug?
GPU dot product

## Slide 14: Example
__global__ void dot(int *mutex, float *a, float *b, float *c) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
float temp = 0;
while (tid < N) {
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// local computation code omitted
if (threadIdx.x== 0) {
lock(mutex);
*c += cache[0];
unlock(mutex);
}
}
__device__ void lock(int *mutex) {
while (atomicCAS(l, 0, 1) != 0 );
}
__device__ void unlock(int *mutex) {
atomicExch(l, 0);
}
GPU dot product

## Slide 15: Example
__global__ void dot(int *mutex, float *a, float *b, float *c) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
float temp = 0;
while (tid < N) { threadfence();
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// local computation code omitted
if (threadIdx.x== 0) {
lock(mutex); threadfence();
*c += cache[0];
unlock(mutex);
}
}
__device__ void lock(int *mutex) { threadfence();
while (atomicCAS(l, 0, 1) != 0 ) threadfence();
}
__device__ void unlock(int *mutex) {threadfence();
atomicExch(l, 0);
}
GPU dot product

## Slide 16: Example
Developed a stress/fuzz testing framework
  Run for 1 hour (~2 seconds per run) and check for errors
GPU dot product

## Slide 17: Example
Developed a stress/fuzz testing framework
  Run for 1 hour (~2 seconds per run) and check for errors
  0 erroneous runs observed
  Did we fix it?
GPU dot product

## Slide 18: Example
  0 erroneous runs observed
  Did we fix it?
Fences cost performance overhead:
60% runtime and energy overhead
GPU dot product

## Slide 19: Example
__global__ void dot(int *mutex, float *a, float *b, float *c) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
float temp = 0;
while (tid < N) { threadfence();
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// local computation code omitted
if (threadIdx.x== 0) {
lock(mutex); threadfence();
*c += cache[0];
unlock(mutex);
}
}
__device__ void lock(int *mutex) { threadfence();
while (atomicCAS(l, 0, 1) != 0 ) threadfence();
}
__device__ void unlock(int *mutex) {threadfence();
atomicExch(l, 0);
}
GPU dot product

## Slide 20: Example
__global__ void dot(int *mutex, float *a, float *b, float *c) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
float temp = 0;
while (tid < N) {
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// local computation code omitted
if (threadIdx.x== 0) {
lock(mutex);
*c += cache[0];
unlock(mutex);
}
}
__device__ void lock(int *mutex) {
while (atomicCAS(l, 0, 1) != 0 );
}
__device__ void unlock(int *mutex) { threadfence();
atomicExch(l, 0);
}
GPU dot product

## Slide 21: Example
  0 erroneous runs observed
  Did we fix it?
Fences cost performance overhead:
60% runtime and energy overhead
GPU dot product

## Slide 22: Example
  0 erroneous runs observed
  Did we fix it?
Fences cost performance overhead:
Less than 3% runtime and energy overhead
GPU dot product

## Slide 23: Example
  0 erroneous runs observed
  Did we fix it?
Fences cost performance overhead:
Empirically fixed, not formally fixed!
GPU dot product

## Slide 24: Roadmap
Background
Testing environment
Environment evaluation
Fence placement

## Slide 25: Roadmap
Background
Testing environment
Environment evaluation
Fence placement

## Slide 26: Weak memory models
consider the test known as message passing (MP)

## Slide 27: Weak memory models
consider the test known as message passing (MP)

## Slide 28: Weak memory models
consider the test known as message passing (MP)

## Slide 29: Weak memory models
consider the test known as message passing (MP)

## Slide 30: Message passing (MP) test
Tests how to implement a handshake idiom
Data
Data

## Slide 31: Message passing (MP) test
Tests how to implement a handshake idiom
Flag
Flag

## Slide 32: Message passing (MP) test
Tests how to implement a handshake idiom
Stale Data

## Slide 38
assertion cannot
be satisfied by interleavings

## Slide 39: Weak memory models
can we assume assertion will never pass?

## Slide 40: Weak memory models
can we assume assertion will never pass? No!

## Slide 41: Weak memory models
what happened?
architectures implement weak memory models where the hardware is allowed to re-order certain memory instructions.
weak memory models can allow weak behaviors (executions that do not correspond to an interleaving)

## Slide 42: Roadmap
Background
Testing environment
Environment evaluation
Fence placement

## Slide 43: Testing environment
Goal: Design a testing environment to reveal weak memory behaviors in GPU applications

## Slide 44: Memory stress
thread 0
thread n
. . . . .
Run application
Application Memory

## Slide 45: Memory stress
thread 0
thread n
extra thread 0
extra thread x
. . . . .
Run application
. . . . .
Memory
stress
Scratchpad Memory
Application Memory

## Slide 46: Litmus tests

## Slide 47: Memory stress
Where to stress:

## Slide 48: Memory stress
Where to stress:
For each distance D:
X
Y
application memory

## Slide 49: Memory stress
Where to stress:
For each distance D:
X
Y
application memory

## Slide 50: Memory stress
Where to stress:
For each distance D:
X
Y
application memory

## Slide 51: Memory stress
Where to stress:
For each distance D:
X
Y
application memory

## Slide 52: Memory stress
Where to stress:
For each distance D:
X
D
Y
application memory

## Slide 53: Memory stress
Where to stress:
For each distance D:
For each scratchpad location I:
X
D
Y
I
application memory
scratchpad memory

## Slide 54: Memory stress
Where to stress:
For each distance D:
For each scratchpad location I:
X
D
Y
I
I
application memory
scratchpad memory

## Slide 55: Memory stress
Where to stress:
For each distance D:
For each scratchpad location I:
X
D
Y
I
I
application memory
scratchpad memory

## Slide 56: Memory stress
Where to stress:
For each distance D:
For each scratchpad location I:
Run MP, SB, LB at distance D litmus tests stressing only location I for 1000 iterations
X
D
Y
I
I
application memory
scratchpad memory

## Slide 57: Memory stress

## Slide 58: Memory stress
Distance D

## Slide 59: Memory stress
Distance D
X
D
Y
application memory

## Slide 60: Memory stress
Distance D
Index I stressed

## Slide 61: Memory stress
Distance D
Index I stressed
I
I
scratchpad memory

## Slide 62: Memory stress
Distance D
Index I stressed
Litmus test

## Slide 63: Memory stress
Vertical bar represents the magnitude of weak behaviors observed

## Slide 64: Memory stress
Visualization samples

## Slide 65: Memory stress
Visualization samples

## Slide 66: Memory stress
Visualization samples

## Slide 67: Memory stress
Visualization samples

## Slide 68: Memory stress
What does this tell us?

## Slide 69: Memory stress
What does this tell us?
To reveal weak behaviors we only need to stress 1 in every 32 locations*
We call a contiguous region of 32 elements a patch
*64 for some chips

## Slide 70: Memory stress
How many patches can we effectively stress?
If D is unknown (as in applications), we would like to stress as many disjoint patches as possible

## Slide 71: Memory stress
Scratchpad has size of 64 patches
We try stressing a randomly selected n patches for values 1 – 64 for n

## Slide 73
Zoom in on first 8

## Slide 75
Stressing 2 random patches is most effective

## Slide 76: Memory stress
Now we have a memory stressing strategy
  Stress two random patches in the scratchpad

## Slide 77: Roadmap
Background
Testing environment
Environment evaluation
Fence placement

## Slide 78: Applications
Observed weak memory issues in 8 applications
7 Nvidia chips (across 3 architectures)
Run applications for 1 hour

## Slide 79: Applications
CHIP | No-stress | Stress
980 |  | 
K5200 |  | 
Titan |  | 
K20c |  | 
770 |  | 
C2075 |  | 
C2050 |  | 

## Slide 80: Applications
CHIP | No-stress | Stress
980 | 0 | 
K5200 | 1 | 
Titan | 0 | 
K20c | 0 | 
770 | 1 | 
C2075 | 0 | 
C2050 | 0 | 

## Slide 81: Applications
CHIP | No-stress | Stress
980 | 0 | 7
K5200 | 1 | 8
Titan | 0 | 8
K20c | 0 | 8
770 | 1 | 8
C2075 | 0 | 8
C2050 | 0 | 8

## Slide 82: Some results:
We provided empirical confirmation of 3 bugs reported in prior work
We discovered unreported weak memory bugs in 2 applications

## Slide 83: Roadmap
Background
Testing environment
Environment evaluation
Fence placement

## Slide 84: Fence insertion
Start with conservative fence placement
Attempt to remove fences
Use our testing framework as an unsound oracle
If errors are observed, put fence back

## Slide 85: Fence insertion
App | Conservative Fences | Reduced Fences
cbe-ht | 10 | 
cbe-dot | 4 | 
ct-octree | 33 | 
tpo-tm | 28 | 
sdk-red | 6 | 
cub-scan | 51 | 
ls-bh | 90 | 

## Slide 86: Fence insertion
App | Conservative Fences | Reduced Fences
cbe-ht | 10 | 1
cbe-dot | 4 | 1
ct-octree | 33 | 1
tpo-tm | 28 | 1
sdk-red | 6 | 1
cub-scan | 51 | 2
ls-bh | 90 | 4

## Slide 87: Fence insertion
Median overhead of reduced fences:
  4% energy
  Less than 3% runtime
Median overhead of consv. Fences
  63% energy
  59% runtime

## Slide 88: Conclusion
Stress/fuzz testing can be used to test applications for weak memory bugs
Stress is best tuned on micro benchmarks
Fences in applications can be costly, but can be reduced with high confidence using stress/fuzz testing
Tyler Sorensen https://www.doc.ic.ac.uk/~tsorensen/
Alastair F. Donaldson http://multicore.doc.ic.ac.uk/